## Slide 1
PISES NEW CAMPUS | AMBASSADOR HIGHLIGHTS DECK
Pakistan International School (English Section), Riyadh | Al Safa Plot | 25,000 m²
SLIDE 1 OF 3
Design Framework & Regulatory Basis
CATEGORY A
TBC Classification
Major Cities (Riyadh)
4.8 m²/student
Education Complex Baseline
(K+Elem+Inter+Sec)/4
25 students/class
Max Classroom Capacity
TBC Mandated Limit
~304 classrooms
7,000-Student Model
Gender-separated G2-G12
~52,400 m²
Total Built-Up Area (BUA)
NET 33,983 m² × Grossing
B + G + 2
Building Configuration
1 Basement + 3 Above Grade
TBC-MANDATED vs NON-TBC DESIGN STANDARDS | CATEGORY A (Riyadh)
Education Level | Area/Student (m²) | Example Net (m²) | Facility | Ratio Rule
Nursery (1m-1yr) | 1.4 (activity) + 0.7 (bed) | 45.0 per room | Activity Room + Bedroom | Per TBC manual
Nursery (1yr-3yr) | 1.8 (activity) + 0.9 (bed) | 45.0 + 22.5 | Activity + Bedroom + Feeding | Per TBC manual
Kindergarten | 2.5 | 62.5 | Classroom + Toilet + Court | Court = ½ class area
Elementary | 1.3 (class) / 1.9 (lab) | 43.12 / 60.1 | Class + Lab + LRC + Art + MPR | 1 Lab per 10 classes
Intermediate | 1.4 (class) / 2.0 (lab) | 45.90 / 62.96 | Class + Labs + LRC + Art + MPR | 1 Lab per 10 classes
Secondary | 1.5 (class) / 2.2 (lab) | 48.12 / 69.9 | Class + Labs + LRC + Art + MPR | 1 Lab per 10 classes
Science Lab (Elem) | 1.9 | 60.1 | General Science Lab | 1 per 10 classrooms
Computer Lab (Elem) | 1.9 | 60.1 | Computer & Languages Lab | TBC unit / qty planned
Learning Resource Ctr | 2.5 | 75.1 | Library / LRC | Librarian 8 m² min
REGULATORY HIERARCHY & NET→GROSS METHODOLOGY
REGULATORY HIERARCHY (Order of Authority):
1. Saudi Building Code (SBC) — Mandatory
2. Civil Defense Regulations — Mandatory
3. Municipal / Balady Requirements — Mandatory
4. TBC Category A Guidelines — Programmatic
5. International Codes (IBC/NFPA) — Reference
▶ Where conflict: more stringent governs
▶ Occupancy: Group E (Educational)
▶ Risk Category III (>250 occupants)
NET → GROSS MULTIPLIERS:
Academic / Admin / SEN: NET × 1.45
High-Service (Labs/Sports): NET × 1.65
Ops / Back-of-House: NET × 1.55
EDUCATION COMPLEX FORMULA:
(K + Elem + Inter + Sec) ÷ 4 = 4.8 m²/student
(5.0 + 4.4 + 4.7 + 5.25) ÷ 4 = 4.8375
Land Baseline: 4.8 m² × 7,000 = 33,600 m²
NON-TBC ITEMS (Best Practice / Institutional Planning Assumptions)
Category | Facilities | Net Area Drivers | Basis
SEN & Wellbeing | Resource Rooms, Therapy, Sensory, Counselling | 736 m² NET | International Best Practice
Food Services | 2× Dining Halls, Kitchen, Servery, Cold Store | 3,380 m² NET | Multi-shift dining model
Sports & PE | 2× Sports Halls, Pool (25m), Changing | 3,981 m² NET | Institutional standard
Auditorium/Commons | 300-seat Auditorium, 2,000 m² Atrium, Exam Hall | 4,070 m² NET | Campus life / events
CONFIDENTIAL | Pakistan International School (English Section), Riyadh | Basis of Design v0.4
Prepared for Ambassador / SMC Briefing

## Slide 2
CAPACITY SCENARIOS | 5,500 / 6,000 / 7,000 STUDENTS
Proportional Scaling from Actual Enrollment (5,263 current) to Design Targets | NET-First Model
SLIDE 2 OF 3
Scenario Comparison & Area Build-Up
CURRENT ENROLLMENT SNAPSHOT (Session 2024-25, as of 31 March 2025)
Segment | Grades | Students | Boys | Girls | Sections | Avg/Section | Classrooms @25 cap
Early Years | Nursery-KG | 801 | 415 | 386 | 55 | 14.6 | 33
Primary | G1–G4 | 1,639 | 839 | 800 | 82 | 20.0 | 66
Intermediate | G5–G9 | 2,051 | 1,042 | 1,009 | 104 | 19.7 | 83
Secondary | G10–G12 | 772 | 394 | 378 | 40 | 19.3 | 31
TOTAL CURRENT: 5,263 students | Boys: 2,690 (51.1%) | Girls: 2,573 (48.9%) | 281 Sections | Morning + Afternoon shifts
SCALING METHODOLOGY (Proportional Distribution from Current Baseline)
STEP 1: Current distribution ratios derived from actual 5,263 enrollment
Early Years 15.2% | Primary 31.1% | Intermediate 39.0% | Secondary 14.7%
STEP 2: Apply ratios to target capacity → derive student count per segment
STEP 3: Classrooms = Students ÷ 25 (TBC max/class) + operational buffer (~8%)
STEP 4: NET area = Classrooms × TBC unit areas + specialist spaces (labs, LRC, etc.)
Specialist ratio: 1 Science Lab per 10 classrooms; 1 ICT Lab per ~15 classes
STEP 5: GROSS (BUA) = NET × grossing factors (1.45 academic / 1.65 high-service)
STEP 6: Gender separation from G2 onwards doubles classroom wings (Boys + Girls)
THREE-SCENARIO CAPACITY COMPARISON | NET-First Computation to BUA & Cost
PARAMETER | UNIT | SCENARIO A 5,500 Students | SCENARIO B 6,000 Students | SCENARIO C 7,000 Students (BoD Target)
STUDENT DISTRIBUTION |  |  |  | 
Early Years (Nursery–KG) | students | 836 | 912 | 1064
Primary (G1–G4) | students | 1710 | 1866 | 2177
Intermediate (G5–G9) | students | 2145 | 2340 | 2730
Secondary (G10–G12) | students | 809 | 882 | 1029
TOTAL CLASSROOMS (incl. buffer) | rooms | 244 | 267 | 311
AREA BUILD-UP |  |  |  | 
Teaching Spaces NET | m² | 11,020 | 12,048 | 14,040
Labs & Specialist NET | m² | 4,550 | 4,940 | 5,720
Support (SEN/Admin/Staff/IT) | m² | 2,440 | 2,570 | 2,999
Shared (Food/Sports/Audit) | m² | 9,097 | 9,798 | 11,431
TOTAL NET AREA | m² | 27,107 | 29,356 | 34,190
TOTAL GROSS / BUA | m² | 41,179 | 44,580 | 51,926
SITE COVERAGE (3 floors) | % | 55% | 59% | 69%
EST. CONSTRUCTION COST (mid) | SAR M | 189–204M | 204–221M | 238–258M
CONFIDENTIAL | Pakistan International School (English Section), Riyadh | Basis of Design v0.4
Prepared for Ambassador / SMC Briefing

## Slide 3
FACILITY REQUIREMENTS BY LEVEL | TIMELINE & COST SCENARIOS
TBC-Mandated Facilities per 10 Classrooms + Construction Delivery Strategy | B + G + 2 Configuration
SLIDE 3 OF 3
Facility Matrix & Implementation Roadmap
TBC-MANDATED FACILITIES PER EDUCATION LEVEL (Category A, per 10 Classrooms)
Facility Type | Nursery | KG | Elementary (Boys/Girls) | Intermediate (Boys/Girls) | Secondary (Boys/Girls) | Basis
Classrooms (max 25/class) | 1.4–1.8 m²/ch | 2.5 m²/ch | 1.3 m²/st | 1.4 m²/st | 1.5 m²/st | TBC
Science Lab | — | — | 1 per 10 cls 60.1 m² | 1 per 10 cls 62.96 m² | 1 per 10 cls 69.9 m² | TBC
Computer/Language Lab | — | — | 60.1 m² | 62.96 m² | 69.9 m² | TBC
Arts Atelier / Vocational | — | — | 41.9 m² | 51.0 m² | 56.7 m² | TBC
Learning Resource Center | — | Multi-media Library | 75.1 m² | 74.7 m² | 88.6 m² | TBC
Multi-Purpose Room | — | — | 42.5 m² | 45.9 m² | 51.0 m² | TBC
Outdoor Pitch/Court | Half class area | Double class area | Min 300 m² pitch | Min 400 m² court | Min 400 m² court | TBC
Toilets | 1.8 m²/15st | 1.8 m²/class | 1.35 m²/20st | 1.35 m²/20st | 1.35 m²/20st | TBC
CLASSROOM & LAB COUNT BY SCENARIO
Segment | Metric | 5,500 Students | 6,000 Students | 7,000 Students
Early Years | Classrooms | 42 | 45 | 53
Primary (G1-G4) | Classrooms | 74 | 81 | 95
Intermediate (G5-G9) | Classrooms | 93 | 102 | 118
Secondary (G10-G12) | Classrooms | 35 | 39 | 45
TOTAL CLASSROOMS | Rooms | 244 | 267 | 311
Science + ICT Labs | Rooms | 70 | 76 | 88
IMPLEMENTATION TIMELINE | DESIGN-BID-BUILD MODEL
Stage | Duration | Cumulative
1. Basis of Design (BoD) | 2–3 months | Month 3
2. Concept Design | 3–4 months | Month 7
3. Schematic Design | 4–6 months | Month 13
4. Detailed Design / IFC | 4–5 months | Month 18
5. Tender & Contractor Award | 2–3 months | Month 21
6. Construction Phase | 18–22 months | Month 43
7. Handover & Commissioning | 2–3 months | Month 46
TOTAL PROJECT DURATION | 30–46 months | ~3–4 years
COST SCENARIO COMPARISON (Excl. Land & Professional Fees)
Scenario | Spec Level | Est. Range (SAR) | OPEX Profile
Code Minimum | VRF, reduced finish | 205–220M | HIGH
Mid-Institutional (Adopted Baseline) | CHW HVAC, mid finish Full ICT, AV included | 240–260M | BALANCED
Enhanced Campus | Premium facade, BMS Advanced acoustics | 270–295M | LOW
+ Contingency (7–10%) | — | +17–30M | —
BUILDING CONFIGURATION: Basement + Ground + Floor 1 + Floor 2 (B + G + 2)
Plot: 25,000 m² | Footprint: ~17,500 m²/floor | Site Coverage: ~70% | Urban high-density model
Basement: Staff parking + MEP plant + Fire tanks + Storage | Above grade: Academic + Shared functions
Delivery: Traditional Design-Bid-Build | Phasing Option: Phase 1 (5,000 cap) + Phase 2 (2,000 expansion)
KEY ASSUMPTIONS & NOTES FOR AMBASSADOR REVIEW:
● All TBC-mandated areas comply with Category A (Riyadh) standards | ● Max 25 students/classroom (TBC) | ● Gender separation from Grade 2 per Saudi regulation
● Non-TBC items (SEN, Food, Sports, Auditorium) follow international best practice | ● Costs are 2025 SAR planning estimates excl. land, fees & inflation | ● 7,000 is design target; current enrollment = 5,263
● NET → GROSS factors: Academic 1.45× / High-service 1.65× / Ops 1.55× | ● Structural & MEP designed for full 7,000 capacity regardless of phasing
CONFIDENTIAL | Pakistan International School (English Section), Riyadh | Basis of Design v0.4
Prepared for Ambassador / SMC Briefing